## Slide 1: Introduction to JITTER

## Slide 2: Timing Errors
Long term variation from the ideal position
Short term variation from the ideal position
The SONET standard states that "Jitter is defined as the short-term variations of a digital signal's significant instants from their ideal positions in time
Jitter Impact the BER
Jitter types
  Random
  Deterministic
Probability histogram showing deterministic and random components
Tail
This is bimodal
response

## Slide 3: Random Jitter
Random Jitter is probabilistic
  Not bounded
  Has a mean and standard deviation
  It is called Gaussian (normal distribution)
  Has no pattern and is not periodic
  Since it is random variable we need N samples
Mean: Mean Value: The arithmetic mean, or average, value of a clock period is the nominal period
Standard Deviation: The standard deviation, represented by sigma (σ), is the average amount by which a measurement varies from its mean value
RJ s measured based on Unit Interval
  1 UI = 1 Period (seconds)

## Slide 4: Random Jitter
Random

## Slide 5: Random Total Jitter
Random Jitter that is not bounded and can be described by a Gaussian probability distribution
  Random jitter is characterized by its standard deviation (rms) value
  Gaussian distributions are symmetrical about a mean value.
  One standard deviation (1σ) is defined as the window which contains 68.26% of a population to one side of the mean.
Each side of the population

## Slide 6: Ideal Time Diagram and Jitter
Jitter can result in error

## Slide 7: Deterministic Jitter
Predictable
It is abounded
Due to source imperfections
Three sub-categories
  Periodic Jitter (sinusoidal)
  Data Dependent Jitter
  Duty-Cycle Dependent

## Slide 8: BER & Total Jitter
To find the probability of a data error occurring, the sum of the probabilities of either data edge being in error must be multiplied by the probability of a transition actually occurring
The probability of a transition actually occurring is represented by the average transition density and assumed to be equal to 50% for a typical data stream
Total jitter is nxRJ + DJ
  n is the number of standard deviations (σ) of random jitter that will produce a data error
  In this expression RJ is in UI (rms) and DJ is in UI
  Note that RJ and DJ are both expressed as peak UI – representing the worst case scenario
For a Gaussian distribution (RJ), for example, 1.28E-10% of samples lie outside a 7s limit to one side of the mean

## Slide 9: BER & Total Jitter- Example
Assume:
  TJ = 0.5UI(pk), DJ = 0.15UI(pk) and RJ = 0.05UI(rms),
  What is BER corresponding to the random jitter?
Total jitter is TJ = nxRJ + DJ
We find n = 7 ; corresponding to 7 Standard Deviation (SD)
  This is the number of SD of random jitter that will produce a single data error
For a Gaussian distribution (RJ), 1.28E-10% of samples lie outside a 7s limit to one side of the mean.
  The total error rate (BER) is then given by samples which lie outside a +/-7s limits to both sides of the mean multiply average transition density (50% of typical data stream)
BER = (1.28E-10% + 1.28E-10%) x 50% = 1.28 E-10%
Remember:
TJ is the total jitter that can be tolerated in order to support the intended BER!

## Slide 10: Periodic

## Slide 11: Data Dependent Jitter
101010
Compared with 1010111
This is acting as LPF
 ISI

## Slide 12: Duty –Cycle Dependent Jitter – Not symmetric

## Slide 13: Jitter Separation

## Slide 14: Total Jitter Example

## Slide 15: Jitter Measurements
Periodic Jitter

## Slide 16: Deterministic Jitter Measurement Techniques
Period Jitter (P1, P2, P3)
Time Interval Error (Per Edge) – if more than 50%  eye is closed!
Cycle-by-Cycle (C2, C3)

## Slide 17: Example
R = 1062.5 Mbps
TIE = 430 psec (0.457 UI)
N (population samples) = 42K
It actually has periodic jitter
components as well!
They are around 0.14 UI –
Cannot be obtained from the pic.