## Slide 1: Introduction to SONET

## Slide 2: Optical Networks
Networks using optical fiber can be thought as client layers of optical layer
  Backbone
  Access
  Metro
Backbone optical fiber client layers
  SONET / SDH
  Ethernet
  Optical Transport Network

## Slide 3: Other Client Layers - Metro
Gigabit Ethernet
10-Gigabit Ethernet
Fibre Channel (storage network)
Resilient Packet Ring (RPR) – packet traffic
SONET/SDH

## Slide 4: SONET/SDH
SONET/SDH: first generation of optical networks deployed in backbone networks
Supports constant bit rate (CBR) connections
Multiplexes CBR connections into higher speed optical connections by using time division multiplexing
Originally designed for low speed voice and CBR connections, up to 51 Mb/s
Supports data network, packet traffic that can have link transmission rates in the tens of gigabits per second.
It provides carrier grade service of high availability

## Slide 5: SONET Layers

## Slide 6: SONET/SDH
Synchronous Optical Network
  Transmission and multiplexing standard for high-speed signals within the carrier infrastructure in North America
SDH (Synchronous Digital Hierarchy), has been adopted in Europe and Japan

## Slide 7: SONET Timing
http://people.seas.harvard.edu/~jones/cscie129/nu_lectures/lecture12/sonet/sonet.html

## Slide 8: Synchronization vs. Plesiochronous
Plesiochronous digital hierarchy (PDH)
  Known as asynchronous digital hierarchy in North America
  Used for multiplexing digital voice circuits
    4KHz Bandwidth
    Sampled at 8KHz
    Bit rate of 64 kbps (basic stream)
    Higher speeds are achieved by multiple of basic stream
In North America the basic voice rate is called digital signal – n
  E.g., DS0, DS1,
In Europe this hierarchy is labeled as E0, E1, E2, E3, & so on

## Slide 9: Plesiochronous - Issues
Each system has its own clock (asynchronous) – nominal clock
  Difference in clock can generate serious synch. Issues
    20 ppm difference between clocks  1.8 kbps bit rate difference
  Bit stuffing is typically used to compensate for difference in transmission rates
    Transmission rates are not exactly integral multiple of the basic rate (64 kbps)
    DS1 (1.544 Mbps) > 24 x 64 kbps !
  In order to extract lower rate the entire signal has to be demultiplexed – expensive!
Provides little/no management information including performance monitoring
Offers little standards for reliability

## Slide 10: SONET / SDH Standards - Advantages
Higher bit rates are integral multiples of lower rates
All clocks are perfectly synchronized (via a master clock)
Incorporate extensive management information, e.g., performance monitoring
Provides interoperability between different devices by different vendors
Fast restoration time (much longer in PDH)

## Slide 11: SONET / SDH Multiplexing
SONET basic rate is 51.84 Mbps
  Called the synchronous transport signal level-1 (STS-1)
  STS is an electrical signal
  It uses scrambling (to avoid long runs of 1s and zeros)
  Higher rate signals (STS-N) are obtained by interleaving N frames
    No need for bit stuffing
    Simple demultiplexing process
Optical interfaces of STS-N are labeled as OC-N

## Slide 12: SONET Hierarchy

## Slide 13: SONET Frame
SONET frame
  Overhead bytes called transport overhead
  Payload
  STS payload is carried in synchronous payload envelope (SPE)
    SPE contains additional path overhead
SONET uses pointers to indicate the location of the payload data within the frame
  Clock phase differences can be compensated using pointer adjustments (no bit stuffing)
    Pointer processing is complex!

## Slide 14: Framing

## Slide 15: SONET Frame
Lower-speed non-SONET streams below the STS-1 rate are mapped into virtual tributaries (VTs)
  Four VT sizes
  SDH uses Virtual Container (VC) to accommodate for lower speed signals
SONET allows multiplexing lower-speed asynchronous streams into Virtual Tributary

## Slide 16: SONET Concatenation
An STS-Nc signal with a locked payload is also defined in the standards
  The “c” stands for concatenated
  N is the number of STS-1 payloads
The concatenated or locked payload implies that this signal cannot be demultiplexed into lower-speed streams
Example: 150 Mb/s client signal can be mapped into an STS-3c signal
How do we use SONET to carry Gigabit Ethernet?
Notes: Use STS48c – 150 percent over provisioning!

## Slide 17: Virtual Concatenation
Virtual Concatenation (VCAT) allows noncontiguous payloads to be combined as a single connection
Such a grouping is referred to as a virtual concatenation group (VCG)
The VCAT notation for SONET
  STS-N -M v
  N is the size of a member & M is the number of members in a VCG
Example: How do we carry GigabitE
STS-3-7V (155 Mbps x 7) about 1.05 (excluding the overhead) – 5 percent overprovisioning!

## Slide 18: SONET Layers
TM: terminal multiplexer (end-to-end) connection
ADM: Add/drop multiplexer
SONET layer consists of four sublayers
  path, line, section, and physical layers
Physical layer interfaces
  Different rates
  Electrical / optical
  Distance (code):
    Intraoffice (short reach) – I
    Short haul 15km/1310 or 40km/1550 - S
    Long haul 40km/1310 or 80km/1550 (400-600 km with Amplifiers) - L
    Very long haul 60km/1310 or 120km/1550
    ultra long haul 160km
Fiber type
  Standard single-mode fiber (G.652)
  Dispersion-shifted fiber (G.653)
  Nonzero dispersion-shifted fiber (G.655)
The transmitter types
  LEDs or multilongitudinal mode (MLM), single-longitudinal mode (SLM) distances
Different Physical Interfaces for SDH (similar for SONET)

## Slide 19: Physical Layer

## Slide 20: SONET Elements
TM: terminal multiplexer (end-to-end) connection
ADM: Add/drop multiplexer
DCS: Digital crossconnect
LTE: Line Terminating Element
UPSR: Unidirectional path-switched rings
BLSR: Bidirectional line-switched rings (with 2 / 4 fibers)
ADM
Is connected to
TM

## Slide 21: SONET Elements
TM: terminal multiplexer (end-to-end) connection
ADM: Add/drop multiplexer
DCS: Digital crossconnect
LTE: Line Terminating Element
UPSR: Unidirectional path-switched rings
BLSR: Bidirectional line-switched rings (with 2 / 4 fibers)
Traffics with the same destinations are groomed together
Unidirectional
Ring
ADM
Is connected to
TM

## Slide 22: IP/SONET over WDM

## Slide 23: SONET Frame Structure
STS-1 frame is 125 usec (1/8000 sec/frame)
There are 810 bytes per frame
  Transmission row-by-row, left-to-right, MSB first

## Slide 24: Frame Structure - Overhead

## Slide 25: Use of Pointers – Pointer H2 Line Overhead

## Slide 26: Frame Structure
A/A2: Network elements use these bytes to determine the start of a new frame
G1 is Yellow alarm to upstream nodes
K2 (FERF) alarm for upstream node
APS indicating automatic switching

## Slide 27: BIP-8 Errors
Monitoring BIPs
  Bit interleaved parity
  Even parity
  Calculated for the previous frame
X/Y = X applies to the first STS-N; Y is remaining

## Slide 28: Calculating BIP-8
Calculated BIP-8 (B1) is based on the previous STS-N frame after scrambling
  Odd parity means there is an error
B2 is based on calculating line overhead of the line overhead – checked by the line terminating equipment

## Slide 29: Client Layers of Optical Fiber

## Slide 30: SONET Protection
Chapter 9 - up to 9.3

## Slide 31: SONET Protection
Availability: A common requirement that the connection will be available 99.999%
Thus network has to be survivable
  continue providing service in the presence of failures
Protection switching is the key technique used to ensure survivability
  The term restoration to schemes where traffic is restored
There are many failures
  Human errors / disasters / Attacks / etc.
  Component failures
  Link failures:
    There are estimates that long-haul networks annually suffer 3 fiber cuts for every 1000 miles of fiber
    For a large network of 30,000 miles of fiber cable, that would be 90 cuts per year

## Slide 32: Protection Key Parameters
Detect failures
Protect against failures (single failures)
Restoration time (60 msec – including detection and restoration)
Topology (Ring / Mesh)
Signaling

## Slide 33: Basic Protection Concepts
Failures must be protected!
Failure types:
  Single / multiple / double (a series of shared links can fail)
Failure example:
  Node / Link (Fiber) / Components
Protection type
  Shared
  Dedicated
Scheme
  Revertive – when shared protection is used
  Non-revertive – when 1+1 is used

## Slide 34: Protection Switching
Automatic Protection Switching (ASP)
Unidirectional
  ASP Required
  Signaling is required
Bidirectional
  No ASP is required
Case b: Only affected direction is switched: - Unidirectional Protection switching (RED is working)
Case c: Bidirectional protection

## Slide 35: Traffic Routing Due to Protection Switching – how the traffic is being rerouted due to link failure
Path Switching
Span Switching
Ring Switching (rerouting on a ring)

## Slide 36: Protection Techniques
1+1 Protection / Simultaneous TX & RX)
1:1 Protection / Signaling is required
To activate the protection / traffic must be switched /
The protection links can carry EXTRA traffic – low priority

## Slide 37: Protection Schemes
1:N Protection / Shared Protection / Signaling is required /
Typically, must be revertive!

## Slide 38: SONET Rings and Self-Healing Rings
Unidirectional path-switched ring (UPSR)
1+1 Protection
Two Fibers only
Unidirectional
Simultaneous traffic (clockwise and counter CW)
Path Layer Protection
Simple / requires no signaling
No node limitation / no length limitation
Note: It is important that the traffics
are moving in DIFFERENT directions
to protect against any node failure

## Slide 39: Four Fiber Bidirectional Lines Switched Ring (BLSR/4)
Mainly, line protection
Traffic is on both directions
  CW and CCW
Max of 16 notes are supported
Max length is 1600 km
Supports span switching or ring switching (next slide)

## Slide 40: SPAN / RING Switching in BLSR/4

## Slide 41: Two-fiber bidirectional line-switched Ring (BLSR/2)
k
Each link has half BW
Very complex – uses APS (K1/K2 bytes)
1:1 Switching
Used for long haul
Very common
Efficient use of special capacity

## Slide 42: Example: BLSR/2 is much more efficient than UPSR (2 fiber)

## Slide 43: Node Failure

## Slide 44: Lab

## Slide 45: Framing Review

## Slide 46: LAB
http://www.cisco.com/en/US/tech/tk482/tk607/technologies_tech_note09186a0080124afa.shtml#f1

## Slide 47: Framing Bytes

## Slide 48: Connection Setup
Pseudo-random bit sequences – max 14 consecutive zeros

## Slide 49: References
http://www.cisco.com/en/US/tech/tk482/tk607/technologies_tech_note09186a0080094313.shtml
http://www.opticus.co.uk/pdf/WhitePaper-Understanding_Error_Checking_Using_Parity_Bytes.pdf